DEBUGGING YOUR NETWORK
Debugging Your Network With Wireshark
Jason Garland
<jgarland@tollfreetollfree.com>

---
Overview
Overview
Topics
  - QoS
  - VLANs
  - Configuring monitor ports for packet captures
  - Capturing intermittent problems with ring buffers
  - Wireshark tips and tricks

---
Problematic Behavior Seen in VoIP
Problematic Behavior Seen in VoIP
Problems:
    - Echo
    - Voice is hard to Understand
    - Voice sounds “Choppy”
    - Delays make conversation difficult
    - Can’t hear other party when speaking
[Speaker Notes: VoIP is sensitive to both]

---
Understanding QoS
Understanding QoS
QoS features affect:
    - Bandwidth
    - Delay
    - Jitter
    - Packet Loss
Managed Unfairness:
    - QoS is both fair and unfair
    - QoS tools improve service for some flows, and degrades service for other flows.
    - With QoS, expediting one packet typically delays another packet.
[Speaker Notes: QoS features affect: Bandwidth – Doesn’t increase or decrease, but effectively utilizes what is there Delay – Latency of the packet as it passes through the network Jitter – If packets are not expedited correctly a device might introduce jitter into the audio stream Packet Loss – No QoS, a voice packet may be just as likely to be dropped as a low priority packet. Managed Unfairness – Expediting one packet typically results in the expense of another packet. Delay: Delay can be introduced by the network or by sip endpoints can cause conversational difficulty can contribute to echo.]

---
Sources of Problems in a Network
Sources of Problems in a Network
All successful VoIP solutions are bound by:
  - Delay (Latency) < 150ms
  - Jitter < 30ms
  - Packet Loss < 1%
Which are hindered by:
  - Network congestion
  - Poor Network design (bandwidth requirements)
  - WAN and LAN bottlenecks
  - Short jitter buffers
  - Lack of RTP preference throughout the call flow
    - RTP packets not tagged as Expedite Forwarding (endpoint configuration)
    - Switch fails to expedite forwarding of RTP (switch configuration)
    - Single point of QoS failure cannot be recovered
[Speaker Notes: All successful VoIP solutions are bound by: Delay – conversational delay, echo – echo must be loud and delayed, 25-50 ms Jitter – will expose jitter to caller - noticeable robotic voice and pops Packet Loss – drops in the audio]

---
Solutions for These Problems
Solutions for These Problems
Technologies that will help these problems are:
    - Quality of Service
    - CAC Call Admission Control
    - VLANs
[Speaker Notes: VLAN – Minimize network traffic by separating broadcast domains Call Admission Control – Limiting call flow according to predetermined capacity limitations. Queuing]

---
DSCP AND TOS
DSCP AND TOS
DSCP - Differentiated Services Code Point
TOS – Type of Service
[Speaker Notes: DSCP/TOS is used to mark packets so that they can be prioritized on the network based on this marking. DSCP - Differentiated Services Code Point TOS – Type of Service]

---
TOS
TOS

---
DSCP
DSCP

---
DSCP/TOS Table
DSCP/TOS Table
[Speaker Notes: The text of this slide is very small. Handouts of this slide should be printed.]

---
Recommendations for Configuring QoS on Cisco Switches
Recommendations for Configuring QoS on Cisco Switches
Configure network infrastructure to honor QoS markings on voice packets.
    - Enable Auto QoS: Cisco Best Practices for VoIP
    - Configure DiffServ trusting on interfaces with SIP endpoints. (Cisco L3 switch): # mls qos trust
[Speaker Notes: Egress CoS Queues: Strict priority scheduling is based on the priority of queues. Packets in the high-priority queue always transmit first, and packets in the low-priority queue do not transmit until all the high-priority queues become empty.]

---
Recommendations for Configuring QoS on Audiocodes Gateway
Recommendations for Configuring QoS on Audiocodes Gateway
Audiocodes Gateway
    - Set to correct DSCP values by default
    - Configurable in GUI
[Speaker Notes: IC – Default (HMP and AudioCodes) Both Platforms mark the RTP packet by default Both Platforms can be modified in IA Polycom Phones sip.cfg file Has to be configured in the .cfg file or is set by default with the Phone Configurator Media Server Enable in Configured with the QoS packet scheduler on the network card - http://www3.inin.com/support/librarydocs/30/WebHelp/mergedProjects/wh_tr/bin/qos_for_the_xic_platform.pdf Audiocodes Gateway – Set by default, configurable in GUI Interaction Gateway Set By default by HMP All the above devices will use DSCP to mark the entire IP header with priority Packets are marked as 10111000. TOS[ DSCP(101110)00] This gives RTP a priority of 5 instead of the default of 0 Network infrastructure still needs configuration]

---
How Does QoS Benefit VoIP Traffic?
How Does QoS Benefit VoIP Traffic?
Packets marked ‘2E’ will be will be placed in high priority queue which will be emptied before anything from low priority queue is sent.
All network devices should use QoS to expedite voice traffic. A single point of QoS failure cannot be recovered.
RTP Packets are marked by SIP endpoint with DSCP value of 101110 or “2E”
All Voice traffic tagged with DSCP value of 101110
All voice traffic forwarded first, resulting in lowest possible delay and jitter.
Network
Layer 3 Switch
SIP Endpoint

---
Using Packet Captures to Troubleshoot
Using Packet Captures to Troubleshoot
Packets are marked by SIP endpoint with DSCP value of 101110 or “EF”
Capturing packets from the egress port will show us the problem.
Problem: Switch is not expediting voice traffic, which causes data traffic to interfere with audio stream
All Voice traffic tagged with DSCP value of 101110
Network
Layer 3 Switch
SIP Endpoint
DevCisco#config term
DevCisco(config)#int fast0/24
DevCisco(config-if)#port monitor fast0/2

---
Voice is Difficult to Understand
Voice is Difficult to Understand
Resolution:
    - This is caused by packet loss or garble from packet loss.
    - Isolate the problem with pcap to determine if the problem is due to dropped packets, jitter due to QoS problems, network congestion, or endpoint buffer problems.
Use packet capture to isolate where jitter or packet loss is introduced
Network
Layer 3 Switch
SIP Endpoint

---
Delay in Conversation
Delay in Conversation
Resolution:
    - Conversational delay due to latency of packets over the network.
    - QoS settings on endpoints/network
    - Lower Endpoint Jitter Buffer
Lower endpoint jitter buffer to just over average jitter
Confirm DSCP is 101110
Measure average jitter
Layer 3 Switch
SIP Endpoint 1
SIP Endpoint 2

---
Voice Sounds “Choppy”
Voice Sounds “Choppy”
Resolution:
    - Normally when a customer reports “Choppy Audio” jitter, or VAD are the culprits.
    - Confirm QoS tagging, and settings on switch. Make sure your jitter buffers are high enough. Also, look for extremely high deltas, which would indicate VAD is enabled.
Use packet capture to look for extremely high deltas in RTP. If present, you should adjust or turn off VAD at SIP Endpoint 1.
Raise endpoint jitter buffer to match average jitter
Confirm DSCP is 101110
Measure average jitter
Layer 3 Switch
SIP Endpoint 1
SIP Endpoint 2

---
Drop in Conversation in Both Directions
Drop in Conversation in Both Directions
Resolution:
    - Audio streams in both directions intermittently drop at the same time due to NICs renegotiating speed and duplex settings.
    - Make sure both switch and SIP endpoints are hard coded as full duplex at 100 Mbps.
A packet capture on this port will reveal lost packets in both streams at once
Gateway
Managed Switch

---
Talk-Over; “Walkie-Talkie” Effect
Talk-Over; “Walkie-Talkie” Effect
Resolution:
    - When one person talks they cannot hear the other party.
    - This can be caused by duplex settings between the SIP endpoint and the switch.
    - Make sure both switch and SIP endpoints are hard coded as full duplex at 100 Mbps.
A packet capture on this port will reveal packets traveling in only one direction at a time
Gateway
Managed Switch

---
Capturing packets
Capturing packets

---
Monitor Ports
Monitor Ports
[Speaker Notes: Source: http://www.cisco.com/en/US/products/hw/switches/ps708/products_tech_note09186a008015c612.shtml]

---
Configuring Monitor Ports
Configuring Monitor Ports
C2950#configure terminal
C2950(config)#
C2950(config)#monitor session 1 source interface fastethernet 0/2
 !--- This configures interface Fast Ethernet 0/2 as source port.
C2950(config)#monitor session 1 destination interface fastethernet 0/3
 !--- This configures interface Fast Ethernet 0/3 as destination port.
[Speaker Notes: Source: http://www.cisco.com/en/US/products/hw/switches/ps708/products_tech_note09186a008015c612.shtml]

---
Verifying Your Monitor Port Config
Verifying Your Monitor Port Config
C2950#show monitor session 1
Session 1
---------
Source Ports:
RX Only: None
TX Only: None
Both: Fa0/2
Destination Ports: Fa0/3
C2950#
[Speaker Notes: Source: http://www.cisco.com/en/US/products/hw/switches/ps708/products_tech_note09186a008015c612.shtml]

---
How to Setup a Ring Buffer Packet Capture
How to Setup a Ring Buffer Packet Capture

---
Setup a Ring Buffer Using Tshark
Setup a Ring Buffer Using Tshark
Identify the interface index number:
C:\>"C:\Program Files\Wireshark\tshark.exe" -D
1. \Device\NPF_GenericDialupAdapter (Adapter for generic dialup and VPN capture)
2. \Device\NPF_{E7CC24DA-6D95-4543-B676-4F07D4A2EFBD} (Cisco Systems VPN Adapter (Microsoft's Packet Scheduler) )
3. \Device\NPF_{08C211F2-3FA7-44D3-881E-E936FC196226} (Broadcom NetXtreme Gigabit Ethernet Driver)

---
Setup a Ring Buffer Using Tshark
Once we have identified the interface we can start our capture.
Create a ring buffer capture with 100 x 50MB files and save them into the TEMP folder:
"C:\Program Files\Wireshark\tshark.exe" -i 3 -w %TEMP%\capture.pcap -b filesize:51200 -b files:100
Also apply a filter:
"C:\Program Files\Wireshark\tshark.exe" -i 3 -o "rtp.heuristic_rtp: TRUE" -w %TEMP%\capture.pcap -b filesize:51200 -b files:100 –R “udp or rtp or sip or icmp or dns or rtcp or t38”

---
Setup a Ring Buffer Using Tshark
Wireshark/Tshark will automatically insert an index number, and a date/time stamp formatted:
capture_XXXXX_YYYMMDDHHMMSS.pcap
Example:
capture_00001_20090304083754.pcap
capture_00002_20090304084133.pcap
…
capture_00099_20090304084423.pcap
capture_00100_20090304084558.pcap
After it gets to 100 files it will delete the oldest file and continue the index:
capture_00101_20090304085056.pcap
capture_00102_20090304085114.pcap
…

---
Merging Captures with Mergecap
Merging Captures with Mergecap
C:\>"c:\Program Files\Wireshark\mergecap.exe" -h
Merge two or more capture files into one.
Usage: mergecap [options] -w <outfile|-> <infile> ...
Output:
  -a	files should be concatenated, not merged
        Default merges based on frame timestamps
  -s <snaplen>	truncate packets to <snaplen> bytes of data
  -w <outfile|->	set the output filename to <outfile> or '-' for stdout
  -F <capture type> set the output file type, default is libpcap
        an empty "-F" option will list the file types
  -T <encap type> set the output file encapsulation type,
        default is the same as the first input file
        an empty "-T" option will list the encapsulation types
Miscellaneous:
  -h display this help and exit
  -v verbose output

---
Merging Captures with Mergecap
Identify the files you want to merge and list them as the input files in chronological order.
Syntax: mergecap.exe –w <outfile> <infile1> <infile2> …
Example:
C:\>"c:\Program Files\Wireshark\mergecap.exe” –w big.pcap capture_00001_20090304083754.pcap capture_00002_20090304084133.pcap

---
Filtering Large pcap Files with Tshark
Filtering Large pcap Files with Tshark
Prepare a Wireshark display filter and apply it to your input file.
Syntax: tshark.exe –r <infile> -w <outfile> -R <Wireshark display filter>
Example:
C:\>"c:\Program Files\Wireshark\tshark.exe” –r big.pcap –w filtered.pcap –R “sip.Call-ID == foo@127.0.0.1 or rtp.ssrc == 1234”
For more information execute tshark with the help switch:
C:\>"c:\Program Files\Wireshark\tshark.exe” -h

---
Demonstration
Demonstration

---
General Demonstration of Tools
General Demonstration of Tools
Wireshark/Ethereal – www.wireshark.org
      - How to setup a Ring Buffer
        - Using Wireshark
        - Using Tshark
      - Merging captures with Mergecap
      - Filtering large captures with Tshark
      - Wireshark tweaks

---
Wireshark Filter examples
Wireshark Filter examples
Filter by SIP Call-ID
sip.Call-ID == "252605206_11120@67.16.109.245"
SIP and RTP
sip && rtp
RTP without correct DSCP value
rtp && ip.dsfield.dscp != 0x2e
Excessive Jitter(30ms+) or Packet loss
rtcp.ssrc.jitter >= 240 || rtcp.ssrc.fraction >= 1
eq	==	Equal
ne	!=	Not Equal
gt	>	Greater Than
lt	<	Less Than
ge	>=	Greater than or Equal to
le	<=	Less than or Equal to
and	&&	Logical AND
or	||	Logical OR
not	!	Logical NOT